## Slide 1
Name: Abdulrahman Omar Abobakr Alamodi
IoT-Enabled ESP32 Mobile Robot for Obstacle Detection and Remote Monitoring
School of Computing and Informatics
Course Name : Internet of Things (IoT)
Course Code : CDE2243
Instructor : Ts. Mohd Zulkifli Mohd Zaki
Group : B
Using ESP32, Ultrasonic Sensor, and ThingSpeak Cloud
Notes: My name is Abudlrahman, and in this video I will present my project titled
“IoT-Enabled Mobile Robot for Obstacle Detection and Remote Monitoring.”
This project was developed using an ESP32 microcontroller, ultrasonic sensing, and a cloud-based IoT dashboard.

## Slide 2
  Implement real-time obstacle detection for safe and autonomous navigation of robots.
  Enable continuous monitoring of sensor data and robot status via a cloud-based dashboard.
  Develop a comprehensive IoT mobile robot system that integrates hardware, software, and cloud components.
Click to edit Master title style
IoT Use Case & Project Goals
The project aims to develop a mobile robot that detects and avoids obstacles while providing remote monitoring capabilities. It enhances automation and safety in various environments.
Notes: The main use case of this project is an IoT-enabled mobile robot designed for obstacle detection and avoidance with remote monitoring in indoor environments.

## Slide 3
System Architecture Overview
System Architecture Diagram
ULTRASONIC SENSO
ESP32 MICROCONTROLLER
DECISION LOGIC
FORWARD / STOP / WARNING
LED INDICATORS
WI-FI COMMUNICATION
THINGSPEAK CLOUD
USER DASHBOARD
Architecture Description
  The ultrasonic sensor measures the distance to nearby obstacles.
  Sensor data is processed locally by the ESP32 microcontroller.
  Based on the distance and battery level:
    The robot decides whether to move forward, stop, or enter warning mode.
  Robot state is represented using LED indicators.
  Selected data is transmitted via Wi-Fi to the ThingSpeak cloud.
  Users can monitor the robot remotely through an IoT dashboard.
Notes: This slide shows the overall system architecture.
The ultrasonic sensor collects distance data and sends it to the ESP32 microcontroller.
The ESP32 processes this data locally and decides whether the robot should move forward, stop, or enter a warning state.
robot state is rep...
Selected data is then transmitted using Wi-Fi to the ThingSpeak cloud platform, where it can be viewed by the user through a dashboard.
This design ensures fast local response while still supporting remote monitoring.

## Slide 4
Hardware Components and Justification
ESP32 Microcontroller
  Acts as the main controller of the robot
  Processes sensor data and executes decision logic
  Built-in Wi-Fi and Bluetooth (future expansion)
  Low power consumption compared to older boards
Ultrasonic Sensor (HC-SR04)
  Measures distance to obstacles in front of the robot
  Used for real-time obstacle detection and avoidance
LED Indicators
  Green LED → Forward movement
  Red LED → Stop
  Yellow LED → Warning/obstacle detected
Simulates motor states and helps visualize robot behavior during simulation.
Battery Monitoring (ADC Input)
  Battery level is monitored using an ESP32 ADC pin
  In simulation, a potentiometer is used to emulate battery voltage changes
Enables power management and low-battery safety behavior.
Resistors
  Protect LEDs from overcurrent
  Standard electronics practice
Notes: Battery monitoring is implemented using an ADC input, which is simulated in Wokwi using a potentiometer.

## Slide 5
Software Design and Decision Logic
Software Structure
The program is divided into clear functional blocks:
  Sensor reading
  Decision-making logic
  Actuation (LED control)
  Wireless communication
  Cloud data upload
Decision Logic Flow
  The ultrasonic sensor continuously measures distance
  Battery level is read using the ESP32 ADC
  If battery level is low:
    Robot enters safe mode
    Movement stops
    Warning indicator is activated
  If battery is normal:
    Distance is checked against a safe threshold
    If obstacle is detected → robot stops
    Otherwise → robot moves forward
Notes: The software is designed around a simple decision-making logic.
First, the ESP32 reads the distance from the ultrasonic sensor and the battery level from the ADC input.
If the battery level is low, the robot enters a safe mode and displays a warning state.
If the battery level is normal, the distance is checked.
If an obstacle is detected, the robot stops. Otherwise, it continues moving forward.
This logic ensures safe and reliable operation.

## Slide 6
Communication Method and Cloud Integration
Wireless Communication
  The ESP32 uses Wi-Fi for communication
  Wi-Fi enables long-range and internet-based connectivity
  Suitable for remote monitoring applications
  Protocol used: HTTP
Cloud Platform
  ThingSpeak is used as the IoT cloud platform
  Receives data from the ESP32 using HTTP requests
  Stores and visualizes data in real time
Data Sent to Cloud
  Distance to obstacle (cm)
  Robot state (Forward / Stop / Warning)
  Battery percentage
  Low battery alert flag
Notes: For communication, the ESP32 uses Wi-Fi and the HTTP protocol.
The ThingSpeak cloud platform is used to store and visualize the data.
The data sent includes distance measurements, robot state, battery percentage, and low-battery alerts.
This allows the robot to be monitored remotely through charts and numeric displays on the dashboard.

## Slide 7
Power Management and Security Considerations
Power Management
  Battery level is monitored using an ESP32 ADC input
  A low-battery threshold triggers a warning state
  Robot enters safe mode to prevent battery damage
  Cloud data is sent every 15 seconds to reduce Wi-Fi power consumption
Benefit:
  Improves energy efficiency and system reliability.
Security Considerations
  ThingSpeak channel is set to private
  Data upload requires a Write API Key
  Prevents unauthorized data access
Design trade-off:
  Simple security is suitable for prototype systems
  Advanced encryption can be added in real deployments
Notes: Power management is an important aspect of this project.
Battery level is continuously monitored, and a low-battery condition triggers a warning and safe stop.
To reduce power consumption, cloud updates are limited to once every 15 seconds.
In terms of security, the ThingSpeak channel is private and requires an API key for data upload, preventing unauthorized access.

## Slide 8
Reflection and Conclusion
This project made me realize how an IoT system is developed as the whole solution and not as a group of elements. The application of the ESP32 microcontroller helped me to understand how sensors, decision logic, wireless communication, and cloud platforms interact in a real-life application. My experience with obstacle detection with the help of an ultrasonic sensor helped me understand how real-time data processing and local decision-making works. Among the valuable lessons was the need to create a balance between the responsiveness of systems and their power utilization that prompted the introduction of the periodic update of cloud-based services and a low-battery alert system. Applying ThingSpeak allowed seeing data remotely and learn the way in which IoT dashboards will aid in monitoring and analyzing. The wokwi simulation, which was applied to testing logic and system behavior, was not based on physical hardware. Generally, this project enhanced my knowledge in the domain of IoT architecture, system scalability and design trade-offs in practice, and it further gave me confidence in building embedded systems and IoT-based systems.

## Slide 10
THANK YOU
Link to vide